## Slide 1: ChannelFinder: A directory service

## Slide 2: Motivation and Objectives
A flat name space restricts seriously:
  Clients need to know all channel names beforehand
  Portable generic clients must be simple
  Apps need full configuration or framework supplied service
Develop a Directory Service
  Generic
    No dependency on installation and local conventions
  Simple and fast (enough)
    Use standards wherever possible
  Provides "query-by-functionality"

## Slide 3
pvManager
Graphene
IOC
CA client (JCA/CAJ)
CSS Core
ChannelFinder Integration
Olog Integration
ChannelFinder
Olog
…
…
DataBrowser
BOY
CSS
IOC
…
IOC
pvA client
IOC
…
v3
AccelUtils
v4
Publish/subscribe
Command/response
v4
Masar
...
pvA
Sim
Test
API
Web based REST services
API
…
Java/Python
…
cf-update
Scripts and utilities
Logbook
…
Web UI and other clients
CA
Core Client Technologies
Data Sources
Aggregation
Visualization
vTypes
Data Definition

## Slide 4: ChannelFinder Data
Set of Channels (unique names)
Each Channel has an arbitrary number of Properties (name/value pairs) and Tags (names)
Each Channel, Property, or Tag has an Owner (group) to allow basic access control
All names and values are strings

## Slide 5: Directory Data

## Slide 6: Channel example
"name":"XF:31IDA-OP{Tbl-Ax:X1}Mtr",
"owner":"train",
"properties":
["handle":"Setpoint",
"axis":"1",
"hostname":"training.org.epics",
"iocName":"motorsim",
"time":"2016-03-21"]
"tags":
["motor",
"sys.XF:31"
]

## Slide 7: Query Example
XF:31*IDA*
  All pvs from the insertion device 31
XF:31*IDA*&axis=4*
  All pvs from the insertion device 31 belonging to axis 4
XF:31*IDA*&axis=4*&pvStatus=active
  All pvs from the insertion device 31 belonging to axis 4
  and with pvStatus active
XF:31*IDA*&axis=4*&tag=aphla.sys.SR
  All pvs from the insertion device 31 belonging to axis 4
  with tag sys.XF:31

## Slide 8: Example Data set

## Slide 9: device FM1G4C02A
Channel Name | SR:C02-MG:G04A{HFCor:FM1} |  | SR:C02-MG:G04A{VFCor:FM1} | 
 | Fld-I | Fld-SP | Fld-I | Fld-SP
handle | READBACK | SETPOINT | READBACK | SETPOINT
elemName | FXM1G4C02A |  | FYM1G4C02A | 
elemType | HFCOR |  | VFCOR | 
elemField | x |  | y | 
devName | FM1G4C02A |  |  | 
sEnd | 65.5222 |  |  | 
cell | C02 |  |  | 
girder | G4 |  |  | 
symmetry | A |  |  | 
length | 0.044 |  |  | 
ordinal | 263 |  | 264 | 
tags | eget | eput | eget | eput
 | x |  | y | 
 | sys.SR |  |  | 

## Slide 10: device FM1G4C02A
Channel Name | SR:C02-MG:G04A{HFCor:FM1} |  | SR:C02-MG:G04A{VFCor:FM1} | 
 | Fld-I | Fld-SP | Fld-I | Fld-SP
hostName | ps-psioc-c02.cs.nsls2.local |  |  | 
iocName | ps-C02A |  |  | 
updateTime | 2015-03-13 |  |  | 
active | True |  |  | 
Tags | archive |  |  | 

## Slide 11: Usage from high level physics
Example*
  corrector = Corrector(deviceName=`FM1G4C02A`)
  >> channels = cf.find(deviceName=‘FM1G4CO2A’)
  xPos, yPos = corrector.getPositions()
  >> xPosPv = cf.find([(deviceName,‘FM1G4CO2A’), (elemField, ‘x’)])
  >> yPosPv = cf.find([(deviceName,‘FM1G4CO2A’), (elemField, ‘y’)])
  >> caget(xPosPv ) and caget(yPosPv )
  corrector.setPositions(xPos=1.23, yPos=3.21)
  ```caput(‘SR:C02-MG:G04A{HFCor:FM1} Fld-SP’, 1.23) and caput(‘SR:C02-MG:G04A{VFCor:FM1} Fld-SP’, 3.21)```
Notes:     High level applications (HLA) deals with thousands of magnets, instruments and more channels.
    Organized/structured channel information is necessary.
    Channels linked to accelerator lattice and diagnostics are even better.
    Searching instead of remembering is easier for HLA users.

## Slide 12: Performance Environment
Database
  150k channels
  40 properties
  60 tags
Queries
  Search using wildcards for channel names and property values
Result Size
  Each channel is 1127 bytes

## Slide 13: CF v3: Large Queries

## Slide 14: Populating ChannelFinder

## Slide 15: Recsync : cfStore
How to add new channels
  Without having to learn the client api's
How to manage existing channels
  Orphaned channels
  Moved channels

## Slide 16: Recsync : cfStore
The record synchronizer
  A client (RecCaster) which runing as part of an EPICS IOC (EPICS support module)
  A server (RecCeiver) which is a stand alone daemon.
Together they work to ensure the the server(s) have a complete list of all records currently provided by the client IOCs.
Recsync Information
  The EPICS Base Version
  A white listed set of environment variables
  The name and type of all records
  Any info() tags associated with these records
https://github.com/mdavidsaver/recsync

## Slide 17: Recsync : cfStore
The properties currently managed with cfStore
  hostName
  iocName
  pvStatus : Active or InActive
  time : The last time the above properties were updated

## Slide 18: cf-properties
Python script part of the CFPropertyManager which populates CF properties using the sites naming convention.
>> CFPropertyManager hostName.iocName.dbl property.cfg
hostName.iocName.dbl
  The output of the dbl command
property.cfg
  A configuration file which defines a list of property name and their corresponding regular expression
  e.g.
  devName=[{][^:}][^:}]*
  devType=[:][^{]*?[:}](?!.*[{])
Thanks to Michael Skinner

## Slide 19: Channel Finder CSS Applications demo
4:26 minutes

## Slide 21: ChannelFinder in CSS
Quick demo of the ChannelFinder applications

## Slide 22: ChannelViewer
CS-Studio  Display  ChannelViewer

## Slide 23: ChannelViewer
Query can be construted for the Name, Property value, Tags associated with channels
Wildcard character like "*", "?" can be used in the queries
prop=val1||val2 is equivalent to prop=val1 OR prop=val2
prop=val1 tag=myTag is equivalent to prop=val1 AND tag=myTag

## Slide 24: ChannelViewer
Channel/s can be forwarded to other cs-studio applications

## Slide 25: ChannelViewer
Channel/s can be forwarded to other cs-studio applications

## Slide 26: ChannelViewer - editing
Add a tag/property to a channel or a group of channels
Remove a tag/property from a channel or a group of channels

## Slide 27: ChannelViewer - editing
Query *X6*Mtr to select all the channels for associated with motor6
Select all pv’s and choose "add property"

## Slide 28: ChannelViewer - editing
Select the property "Axis" from the listed properties.
Enter a value for the property e.g. “X6"

## Slide 29: Channel Tree
Channel Tree by Property allows to create an hierarchical view of the channels by using properties and their values.

## Slide 30: Channel Tree
Query: XF:31*Mtr* handle=Setpoint||Readback
Configure the tree by selecting the properties to be used to create the hierarchy (hostname, handle, axis,…)
Notes: Exercise: create the tree

## Slide 31: Channel Orchestrator
The channel orchestrator is a tool to assist in preparing and writing a group of set points

## Slide 32: ChannelFinder & BOY
Dedicated ChannelFinder widgets
Notes: channelviewer

## Slide 33: ChannelFinder & BOY
Embed channel tree by property widget into the opi
  Set Channel query: “XF:31*Mtr*”
  Tree Properties: iocName, axis, handle
  Selection Expression: #(axis)
Selections from this widget can be used to initialize other widgets

## Slide 34: cfQuery
Accessing channelfinder data in opi screens
=cfQuery(Vstring query) : VTable

## Slide 35: cfQuery
Combining cfQuery with other formulas to create tables/arrays which can be then used with existing cs-studio widgets
=columnOf(pvs(columnOf(cfQuery("*XF:31*Mtr* handle=Readback"), "Name")),"Value")

## Slide 36: ChannelFinder & BOY
Notes: Orchestrator and histogram

## Slide 37: ChannelFinder & BOY
Notes: Orchestrator and histogram

## Slide 38: PVA ChannelFinder in CSS
EPICS7 directory service

## Slide 39: pvaChannelFinder
A EPICS7 RPC service
Request is a NTURI
name, tag, or property value
* & % wildcard chars
Result is a NTTable
List of all the matching channels and their associated properties and tags

## Slide 40: pvaChannelFinder
Filtering
The query defines the tags and properties to be included in the result
Improves performance

## Slide 41: pvaChannelFinder
Pagination
The result can be fetched in parts using the _size and _from arguments
Results in the creation for more robust and responsive clients

## Slide 42: Questions