## Slide 1: Getting started with cs-studio:

## Slide 2: Running CS-Studio
Running cs-studio from command line
  train@training:~/cs-studio$ ./cs-studio-with-pref
Notes: NSLS2

## Slide 3: Running CS-Studio
You can also install cs-studio yourself by downloading and unzipping the appropriate .zip file from
  http://controlsystemstudio.org/download.html
  ~$: ./cs-studio
There are multiple versions of the cs-studio product. Customized for different sites and use cases
Notes: NSLS2

## Slide 4: Welcome
First Steps
Tutorials
What’s New
Help  Welcome

## Slide 5: Workbench
It represents your working environment.
Window
Menu bar
Toolbar
Perspective bar
Views

## Slide 6: CS-Studio: Probe

## Slide 7: Probe
A simple application to connect to pv’s
  Monitor pv’s (caget, camonitor)
  Write to pv’s (caput)
Opening probe
  Menu: CSS  Diagnostic Tools  Probe
  Toolbar:
  Context Menu*: Process Variable  Probe

## Slide 8: Probe - getting started
Connect to a simple scalar pv (simulation)
  In the PV Formula field type “sim://noise” and hit the return key
Connect to a simple scalar pv (IOC)*
  In the PV Formula field type “XF:31IDA-OP{Tbl-Ax:X1}Mtr.RBV” and hit the return key
  * Start the test IOC
  >> cd ~/Epics/iocs/motorsim >> ./startSimMotor.sh
Notes: TODO: pv name

## Slide 9: Probe - deciphering the data
Value:
  Shows the current value of the pv and the timestamp associated with it
Change Value:
  The new value field is used to write new values to the pv If the pv is read only this field is disabled
MetaData:
  Additional information about the pv Type, Display limits, Alarm limits, units…..

## Slide 10: Probe - deciphering the data
The drop down menu allows you to selected the additional information about the pv and the connection to be displayed
  Viewer
  Value
  Change value
  Details

## Slide 11: Probe - writing a value
Connect to a simple scalar pv (local)
  In the PV Formula: field type “loc://my_test_pv(0)” and hit RETURN
  In the New Value: field enter any valid number and hit RETURN

## Slide 12: Probe - writing a value
Open 2 probes
Move the probe views so that they can be both viewed simultaneously
In the first probe enter the setpoint pv PV: XF:31IDA-OP{Tbl-Ax:X1}Mtr
In the second probe enter the Readback pv PV: XF:31IDA-OP{Tbl-Ax:X1}Mtr.RBV
Set a new motor position (-100 and 100)

## Slide 13: Probe - Autocomplete
Autocomplete
  History
  ChannelFinder
  Predefined simulation pv’s (Datasources)
  Formula functions
Notes: TODO: add autocomplete for softIOC pv

## Slide 14: Probe - Help
Help  Help Content
  CSS Applications  Diagnostic Tools  Probe

## Slide 15: Probe – process variable (Datasource)
type://some_pv_name
Datasources
  System (sys://)
  Local (loc://)
  Simulation (sim://)
  File(file://)
  PVAccess (pva://)
Help
  CSS Core  Process Variables

## Slide 16: Probe - Autocomplete Datasources
Autocomplete will list the various pv’s available for a particular datasource
Figure 1

## Slide 17: Probe - pv’s and formulas
Formulas
  Mathematical operations
  Logical operations
  Array operations
  Create/modify tables and arrays
Start with a ‘=‘
Don’t use formulas for things that should be done in the IOC

## Slide 18: Probe - pv’s and formulas
CSS 
Debugging 
Formula Functions

## Slide 19: Probe - Autocomplete formula
Figure 1: Autocomplete will list the formula functions matching your text.
Figure 2: Autocomplete will help you fill the formula function with the correct parameters.
Figure 1
Figure 2

## Slide 20: CS-Studio and PVAccess

## Slide 21: Creating EPICS7 channels pva datasource
The pvaccess datasource prefix when creating the channel pva://<name>

## Slide 22: Creating EPICS7 channels pva datasource
Use the pvacess datasource prefix when creating the channel pva://pvcounter epics:nt/NTScalar:1.0 -> Vdouble

## Slide 23: Accessing EPICS7 structured data
The pva module provides the mapping for NTTypes to Vtypes
Currently supported NTTypes includes
General Normative Types
  NTScalar
  NTScalarArray
  NTEnum
  NTTable
Specific Normative Types
  NTMultiChannel
  NTNDArray

## Slide 24: Accessing EPICS7 structured data
Formula Functions Allow parsing of any EPICS7 data structure into a Type that can be used by cs-studio applications

## Slide 25: Accessing EPICS7 structured data
NTNDArray formula set
image
Creates an VImage from the NTNDArray using all the appropriate fields (value, dimensions, …)
ndArray
Extracts the raw values as a VNumberArray
attributes
Creates a VTable from the attributes structure of this NTNDArray